## Slide 1: SMART INDIA HACKATHON 2026
SETU · INTELLIGENT DEAD RECKONING
Problem Statement ID – SIH26168
Problem Statement Title- AI-ML based Intelligent Dead Reckoning system for seamless navigation
Theme- Smart Vehicles
PS Category- Software
Team ID- N/A
Team Name - Sanskari<CODERS>
TEAM Sanskari<CODERS> Lakshya Jain (Team Leader) · Akshit Jain · Veneya Kharkhodi · Garv Goel · Lavish Kumar · Aashi Jain

## Slide 2: SETU — NAVIGATION WITHOUT GNSS
Sanskari
<CODERS>
When GPS disappears, today's apps freeze, jump, or call the turn too late. SETU keeps your position moving correctly on the map, using nothing but the sensors already inside the phone.
Detailed explanation of the proposed solution
An Android app and a small on-device engine. No dongle, no extra hardware, no internet.
The phone hears the wheels.
Spinning wheels shake the car, and the shake speeds up as you do. The app reads that pitch, so it measures speed instead of guessing it from acceleration — the way a mechanic listens to an engine.
Every turn re-checks the speed.
In a bend, the sideways push divided by how sharply you are turning gives the exact speed — free calibration several times a minute, and it works on a leaning two-wheeler too.
The road becomes the ruler.
The phone knows how much it has turned; the offline map knows the shape of every road. Line the two up and your position falls into place with no satellites at all.
How it addresses the problem
The graph answers one question: after a kilometre with no GPS, how far off are you?
Pure inertial · 180 m — acceleration simply added up — tiny errors compound, so you are a block away after one minute.
Best published phone result · 31 m — error grows steadily with distance, 3.1 % of every kilometre.
SETU · 8.5 m — the line drops each time we recognise something — a bend whose shape matches the map, or a tunnel's magnetic signature. Error is reset instead of piling up.
Innovation and uniqueness of the solution
N1 Speed read from frequency
N2 Two-wheeler lean physics
N3 Scale-free map registration
N4 CAN wheel speeds as teacher
N5 Learned σ and Q in one filter

## Slide 3: TECHNICAL APPROACH
Sanskari
<CODERS>
Methodology and process for implementation
CLIENT
RUNTIME
offline
zero network calls
SYNC
PLANE
out-of-band
async, never blocking
CLOUD
PLANE
batch
region-sharded
SENSE
IMU 200–400 Hz
GNSS raw NavIC L5
Baro Magnetometer
External IMU MEMS / FOG
CONDITION
STFT harmonic ridge
Notch engine order
Shock pothole reject
ACE mount solve
OBSERVE
SVO
spectral speed
CTS
turn speed
CSA
map arc length
EFA
field anchors
NHC
zero side-slip
GQM
sat trust
FUSE
RI-EKF SE₂(3)
learned σ per measurement
learned Q transformer
RB-PF road graph
DELIVER
10 Hz phone pose
200 Hz edge pose
Lane-level + tube
API gRPC · NMEA
DISTRIBUTION signed, immutable, versioned bundles — installed offline
Model registry
Map / tile CDN
Config & flags
CONTRIBUTION opt-in · ~1 KB per edge · signatures only, never trajectories
API gateway
Stream queue
k-anon aggregator
MAP BUILD per region, independently
OSM extract
Graph + κ(s) LUT
DEM · PMTiles
LEARNING nightly retrain, gated on the benchmark
Data lake
Training cluster
Eval gate
Telemetry & KPI
SCALES BY SHARDING, NOT BY CAPACITY zero runtime API calls, so device count adds no serving load · ≤250 MB per region · immutable CDN bundles · contribution ~1 KB per edge
Technologies to be used
Training
PyTorch · Lightning · Hydra · MLflow · masked-IMU pretraining
On-device
LiteRT + XNNPACK · ExecuTorch · int8 QAT · 3.6 MB total
Engine
C++20 · Eigen · SE₂(3) Lie · FlatBuffers · GTest replay
Mobile
Kotlin · Compose · MapLibre + PMTiles · SensorDirectChannel
Edge & maps
aarch64 · gRPC / NMEA / ROS 2 · osmium · CartoDEM

## Slide 4: FEASIBILITY AND VIABILITY
Sanskari
<CODERS>
Analysis of the feasibility of the idea
Data already in hand
IO-VNBD: 5,700 km, phone IMU and CAN bus recorded together
Core physics is closed-form
v = a_lat/Ω and f = v/2πR are algebra; only residuals learn
Fits today's phones
3.6 MB int8, 2.7 ms per tick, CPU only — no NPU needed
Sensors already present
IMU, magnetometer, barometer, raw GNSS with NavIC L5
Maps fit offline
≤250 MB per metro region, no connectivity at runtime
Nothing to buy or fit
no dongle, no encoder, no roadside infrastructure
Every device class clears the ceiling. IO-VNBD's 10 Hz stream is Tier C.
Potential challenges and risks | Severity | Strategies for overcoming these challenges
CSA ambiguous on featureless or badly-mapped roads | High | Landmark saliency scoring · top-k hypotheses in the particle filter · honest σ. Falls back to classical HMM map matching.
Axle harmonics weak — smooth road, quiet EV, soft mount | Medium | Mount-quality gate · summation over 8+ orders · learned σ down-weights it. Falls back to Tier B.
IO-VNBD phone stream is 10 Hz, so cannot validate SVO | Known | Declared as capability tiers. SVO validated on self-collected 400 Hz logs.
No two-wheeler data in IO-VNBD — four cars, no Indian roads | Known | Lean relation imposed as a physics loss, so few samples suffice. Dedicated collection.
Sensor rate throttled below 200 Hz on some devices | Medium | Tier detected at runtime · SensorDirectChannel · verified on three device classes.
Uneven OpenStreetMap geometry on Indian roads | Medium | Covariance scaled by OSM confidence · explicit off-road particle · provider adapter.
Fallback ladder lose CSA → HMM map matching · lose SVO → Tier B · lose both → INS + NHC + ZUPT, already inside the 10 % gate. No single failure leaves us with nothing to show.

## Slide 5: IMPACT AND BENEFITS
Sanskari
<CODERS>
Potential impact on the target audience
Delivery and quick-commerce riders
the next turn is announced before the exit, not after it
Logistics and fleet operators
mileage, ETA and proof of delivery survive the gap — no dongle
Ride-hailing drivers and riders
no frozen or teleporting car; pickups on the correct side
Emergency responders
a live position underground, where dispatch loses them today
Two-wheeler riders
India's largest vehicle class, finally with lean-aware physics
Defence and critical logistics
self-contained; degrades gracefully under jamming or spoofing
Where it matters most
Long tunnels and metro underpasses the road is one-dimensional, so the map carries it
Multi-level parking helical ramps are unique signatures; the barometer gives the floor
Dense urban canyons position unusable, but Doppler velocity survives on 3–4 satellites
Forested and valley highways partial GNSS, absorbed by the trust ramp with no mode switch
Benefits of the solution (social, economic, environmental, etc.)
Social
A correct instruction on time means fewer glances at the screen when a rider can least afford one. Emergency crews stay locatable underground. Accurate navigation stops being a feature of expensive cars.
Economic
Zero marginal hardware — it runs on phones riders already own. No dongle per vehicle, no factory INS, no leaky-feeder per tunnel. Fewer missed exits and failed deliveries on the same fleet.
Environmental
A missed exit is wasted kilometres, fuel and emissions; removing the cause removes all three. Entirely on-device, so no roadside infrastructure is built, powered or maintained.
Strategic
Jamming- and spoofing-resilient by construction, since every channel is self-contained. Uses NavIC L5 where Indian devices expose it, runs fully offline, keeps data on the phone.
Pure inertial
180 m
½·b·t² — a block away after one minute
Best published
31 m
3.1 % per km, INS + NHC in a real tunnel
SETU target
8–15 m
0.8–1.5 % per km, anchored to map and field
Horizontal drift over a 1 km blackout at 60 km/h. The SIH ceiling is 10 % — 100 m.
Reach any Android phone already on the dashboard — no purchase, no fitting, no connectivity. The same engine serves a FOG-grade edge unit at 200 Hz.

## Slide 6: RESEARCH AND REFERENCES
Sanskari
<CODERS>
Details / Links of the reference and research work
DATASET AND BENCHMARK
IO-VNBD: Inertial & Odometry Benchmark Dataset
Data in Brief 35:106885, 2021 · github.com/onyekpeu/IO-VNBD · arXiv:2005.01701
WhONet: Wheel Odometry Neural Network
Eng. Appl. of AI, 2021 · arXiv:2104.02581 — our privileged upper bound
R-WhONet: recalibration by transfer learning
arXiv:2209.05877 — evidence of cross-vehicle domain shift
LEARNED INERTIAL ODOMETRY
Deep Learning for Inertial Positioning: A Survey
Chen & Pan · IEEE T-ITS, 2024 · arXiv:2303.03757
Inertial Navigation Meets Deep Learning
Cohen & Klein · 2024 · arXiv:2307.00014
AI-IMU Dead-Reckoning — invariant EKF
Brossard, Barrau & Bonnabel · IEEE T-IV, 2020 · arXiv:1904.06064
TLIO: Tight Learned Inertial Odometry
Liu et al. · IEEE RA-L, 2020 · arXiv:2007.01867 — learned covariance
OdoNet: untethered speed aiding
arXiv:2109.03091 · 68 % error reduction over NHC alone
CarSpeedNet: accelerometer-only speed
arXiv:2401.07468 · <0.72 m/s ≈ 4.3 % — the accuracy to beat
LEARNED AND ADAPTIVE FUSION
KalmanNet: NN-aided Kalman filtering
Revach, Shlezinger, van Sloun & Eldar · IEEE TSP, 2022
A-KIT: Adaptive Kalman-Informed Transformer
arXiv:2401.09987 · github.com/ansfl/A-KIT — learned process noise
PiDR: Physics-Informed Inertial Dead Reckoning
Sahoo & Klein · 2026 · arXiv:2601.03040
Differentiable particle filters, semi-supervised
arXiv:2011.05748 — end-to-end learning with algorithmic priors
MAP MATCHING AND CONSTRAINTS
Hidden Markov Map Matching
Newson & Krumm · ACM SIGSPATIAL, 2009 — the baseline
Heading–length sequence matching
arXiv:2005.13704 — nearest prior art to CSA; needs a known speed
Map-aided dead reckoning from OBD speed
arXiv:1611.07910
Lever-arm accuracy of the non-holonomic constraint
Zhang & Hu · IEEE TVT, 2020
NHC-assisted GNSS/SINS with motion-state CNN
GPS Solutions, 2023 · doi 10.1007/s10291-023-01483-9
SPECTRAL SPEED AND FIELD ANCHORS
Vehicle Speed Tracking Using Chassis Vibrations
Linköping University, 2016 — axle-order tracking, motivates tunnels
Accelerometer-based wheel odometer
Sensors, 2021 · PMC7918720
Magnetic positioning in a long tunnel
Applied Sciences 11(24):11641, 2021
Vehicle positioning in tunnels: a review
Complex & Intelligent Systems, 2025
Barometric floor detection on smartphones
Sensors, 2015 · PMC4431287 — basis for the parking-level anchor
GNSS INTEGRITY AND PLATFORM
Vehicle positioning underground using a smartphone
ISPRS Archives XLVI-3/W1, 2022 — the 3.1 %/km reference
GNSS multipath detection by machine learning
Hsu · IEEE ITSC, 2017
Android GnssMeasurement HAL — raw observables
source.android.com · pseudorange, Doppler, C/N₀, AGC
u-blox Untethered Dead Reckoning (UDR)
u-blox.com — the closest commercial analogue, on dedicated hardware